Supplier Evaluation – Evaluation Criteria

Contents

1	Overall evaluation	1

2	Main criterion Quality Performance QZ	2

2.1	Mass Production Quality QZ 1	2

2.2	Defective Quantity QZ 2 (ppm)	3

2.3	Certification QZ 3	3

2.4	Sample Quality QZ 4	4

3	Main criterion Delivery Performance LZ	5

3.1	Date Reliability (LZ 1) and Quantity Reliability (LZ 2)	5

3.2	Logistics Quality LZ 3	6

4	Evaluation parameters	7

Note:

The most significant changes compared with the previous version of November 2008 are displayed in green text below.

# Overall evaluation

Schaeffler evaluates the performance of its suppliers on the basis of the evaluation criteria described below. This applies to products and services supplied to defined commodities within Schaeffler, see section 4.

The Overall Performance Indicator GKZ for the Supplier Evaluation comprises the two main criteria of Quality Performance QZ and Delivery Performance LZ, which are weighted as follows:

| Abbreviation | Main criterion | Weighting |
| --- | --- | --- |
| QZ | Quality Performance | 65% |
| LZ | Delivery Performance | 35% |

The Overall Performance Indicator GKZ is defined as

GKZ = 0,65 x QZ + 0,35 x LZ

Note: Evaluation criteria which are not used for the purposes of the evaluation must be set to "0" in the evaluation system.

# Main criterion Quality Performance QZ

The main criterion of Quality Performance QZ comprises the four sub-criteria QZ 1 to QZ 4 illustrated in the following overview that each have different weightings:

| Abbreviation | Sub-criterion | Weighting | Type(s) of claim 1) | Coding 1) |
| --- | --- | --- | --- | --- |
| QZ 1 | Mass Production Quality | 50 % | Complaint for mass production | P003 |
| QZ 2 | Defective Quantity (ppm) | 30 % | Complaint for accumulated scrap | P003 S001 |
| QZ 3 | Certification | 10 % | - | - |
| QZ 4 | Sample Quality | 10 % | Complaint for samples M4, M5 and M6 2) | P002 |

- For information within Schaeffler only

- Schaeffler sample types: initial volume production sample M4, modification sample M5 and repeat sample M6

The formula for calculating the criterion Quality Performance QZ is as follows:

QZ = 0,5 x QZ 1 + 0,3 x QZ 2 + 0,1 x QZ 3 + 0,1 x QZ 4

The quality criteria QZ 1, QZ 2 and QZ 4 are determined by evaluating the justified complaints (with status either open or closed) occurring within a defined assessment period.

This is based on complaints from goods inward inspection, ongoing production and concerns from Schaeffler customers that are caused by the supplier.

## Mass Production Quality QZ 1

The criterion of Mass Production Quality QZ 1 is generated from the ratio between the number of complaints on mass production parts and the number of goods receipt items (included on the delivery note).

Complaints are based on deviations from the product specification (dimensions, material, surface, etc.).

The formula for calculating the criterion QZ 1 is as follows:

| QZ 1 = 100 – 1000 x | Number of complaints (number of cases) mass production |  |
| --- | --- | --- |
|  | Number of goods receipt items in total |  |

If the calculated value is less than 1, a value of 1 is always assigned in accordance with the definition to QZ 1 for technical reasons. If 10% of deliveries are the subject of concerns, the QZ 1 value is therefore 1 instead of 0.

## Defective Quantity QZ 2 (ppm)

The standard formula for determining ppm values on the basis of quantity is defined as:

| ppm value 1) = | Rejected quantity delivered | x 1 000 000 |  |
| --- | --- | --- | --- |
|  | Total quantity delivered |  |  |

- ppm = parts per million

The following applies to the formula for calculating the criterion QZ 2:

| QZ 2 = 100 – B x | ppm value |  |
| --- | --- | --- |
|  | 100 |  |

The commodity factor B (see section 4) is used when calculating the defective quantity in order to compensate for the differing requirements specific to technologies or product groups. If the calculated value is less than 1, a value of 1 is always assigned in accordance with the definition to QZ 2 for technical reasons.

Adjustment of ppm values

If material deliveries are returned, the supplier is required to determine the actual defective quantity and, if there is a discrepancy relative to the quantity rejected by Schaeffler, to notify the Schaeffler location submitting the concern.

If this occurs within a period of two months following the receipt of the goods in the concern at the supplier, the ppm values can be adjusted on the system by the Quality function of the Schaeffler location. Otherwise, the total quantity in the concern will be included as being defective in the calculation of QZ 2.

## Certification QZ 3

In line with the requirements of its customers, Schaeffler has introduced quality management systems to ISO/TS 16949 (Automotive), IRIS (Rail) and AS 9100 (Aerospace), as well as an environmental management system to ISO 14001 and requests appropriate certificates from its suppliers.

For the Schaeffler certificate(s) held by the supplier, points are awarded as follows for the criterion Certification QZ 3 :

| Certification | Points |
| --- | --- |
|  | 1) | 2) |
| ISO/TS 16949, AS 9100, NADCAP or IRIS plus environmental certification in accordance with ISO 14001 or EMAS | 100 | 100 |
| ISO 9001 plus environmental certification in accordance with ISO 14001 or EMAS | 90 | 100 |
| ISO/TS 16949, AS 9100, NADCAP or IRIS | 80 | 90 |
| ISO 9001 | 70 | 80 |
| Escalation status New Business Hold | 1 | 1 |
| No QM system present or quality certificate expired 3) | 1 | 1 |

- Production material suppliers

- Suppliers of part-specific tooling, plastic injection moulding tooling, packing materials 
(Schaeffler commodities M051, M052 and M111)

- System-related by definition "1" point

Escalation status New Business Hold

If Schaeffler imposes the escalation status New Business Hold (see QAA / S 296001 Part 6 - Escalation process) on a supplier during an ongoing assessment period, the Quality Criterion QZ 3 - irrespective of any valid certifications - will be downgraded by definition to 1 point.

The number of points originally awarded, e. g. 70 points for existing ISO 9001 certification, will only be awarded again during the subsequent evaluation period once the status New Business Hold has been rescinded.

## Sample Quality QZ 4

The procedure for the criterion Sample Quality QZ 4 is the same as for the criterion Mass Production Quality QZ 1.

Complaints are based on deviations from the sample specification (dimensions, material, surface, etc.).

The formula for calculating the criterion QZ 4 is as follows:

| QZ 4 = 100 – 500 x | Number of complaints (number of cases) on samples |  |
| --- | --- | --- |
|  | Number of goods receipt items in total |  |

If the calculated value is less than 1, a value of 1 is always assigned in accordance with the definition to QZ 4. If 20 % of sample deliveries are the subject of concerns, the QZ 4 value is therefore 1 instead of 0.

# Main criterion Delivery Performance LZ

The second main criterion of the Supplier Evaluation, Delivery Performance LZ, comprises three sub-criteria that have different weightings:

| Abbreviation | Sub-criterion | Weighting | Type of claim 1) | Coding 1) |
| --- | --- | --- | --- | --- |
|  |  |  | 2) | 3) |  |  |
| LZ 1 | Date Reliability | 40 % | 0 % | 40 % | - |  |
| LZ 2 | Quantity Reliability | 40 % | 0 % | 0 % | - |  |
| LZ 3 | Logistics Quality | 20 % | 100 % | 20 % | Complaint on logistics | L001 |

- For information within Schaeffler only

- Suppliers involved in subcontract work, coatings and heat treatment 
(Schaeffler commodities M380, M381 und M382)

- Suppliers of type-dependant tools (Schaeffler commodity M051)

The formula for calculating the criterion Delivery Performance LZ is:

| LZ = | 0,4 x LZ 1 + 0,4 x LZ 2 + 0,2 x LZ 3 |  |
| --- | --- | --- |
|  | 0,4 + 0,4 + 0,2 |  |

Should individual partial criteria not be used for the purposes of evaluation, the weighting of the remaining criteria is adapted according to example 3) as in the table above, here without Quantity Reliability LZ 2:

| LZ = | 0,4 x LZ 1 + 0,2 x LZ 3 |  |
| --- | --- | --- |
|  | 0,4 + 0,2 |  |

## Date Reliability (LZ 1) and Quantity Reliability (LZ 2)

The criteria for Date Reliability LZ 1 and Quantity Reliability LZ 2 are generally calculated in accordance with a standardised evaluation scheme.

For each delivery, the system compares the required date and required quantity notified by a supplier in advance to the Schaeffler Supply Chain or Purchasing with the actual data determined for the delivery date and delivery quantity at goods inward. The evaluations from the individual deliveries within the evaluation period are each consolidated into a date reliability and quantity reliability.

Depending on the system requirements of individual Schaeffler locations, the evaluation method and scheme for calculating date- and quantity reliability may vary.

Special case

The delivery performance of suppliers involved in subcontract work, coatings and heat treatment is evaluated using the criterion Logistics Quality LZ 3 only.

## Logistics Quality LZ 3

The criterion Logistics Quality LZ 3 is calculated on the same basis as QZ 1 using logistics complaints occurring within the evaluation period in relation to volume products.

In particular, logistics complaints include missing documentation, packaging errors, damage to packaging, delays in delivery which are associated with additional outlay for Schaeffler and production line stoppages at Schaeffler or at the premises of its customers.

Note

In the case of automotive applications, Schaeffler is under an obligation in accordance with ISO/TS 16949 (see section 7.4.3.2) to monitor all occurrences associated with additional freight costs. Accordingly, the suppliers are also under an obligation to notify the Purchasing function of the affected Schaeffler location in writing of such occurrences, if the Purchasing function is not yet aware of these.

Occurrences associated with additional freight costs are included as logistics complaints in the calculation of Logistics Quality LZ 3, irrespective of whether these are recorded by Schaeffler or declared by suppliers.

The following applies to the calculation of the criterion Logistics Quality LZ 3:

| LZ 3 = 100 – 1000 x | Number of logistics complaints (number of cases) |  |
| --- | --- | --- |
|  | Number of goods receipt items in total |  |

If the calculated value is less than 1, a value of 1 is always assigned in accordance with the definition to LZ 3. If 10% of deliveries are the subject of concerns, the LZ 3 value is therefore 1 instead of 0.

# Evaluation parameters

The evaluation parameters underlying the calculation formulae are listed in the following table.

| No. | Commodity | B factor | ppm limit |
| --- | --- | --- | --- |
| M011 | Bar / wire | 1 | 1000 |
| M012 | Tube | 1 | 1000 |
| M013 | Cold rolled strip | 1 | 1000 |
| M014 | Rolled rings | 1 | 1000 |
| M016 | Forged parts | 1 | 1000 |
| M017 | Profiles | 4 | 250 |
| M018 | Hot rolled strip | 1 | 1000 |
| M019 | Drawn wire | 4 | 250 |
| M021 | Non-ferrous metals | 4 | 250 |
| M031 | Plastic granulates | 4 | 250 |
| M032 | Plastic semi-finished products | 4 | 250 |
| M033 | Raw material facings | 4 | 250 |
| M051 | Type-dependant tools | 0,4 | 2500 |
| M052 | Plastic injection moulds | 0,4 | 2500 |
| M141 | Oils and greases for production | 4 | 250 |
| M310 | Plastic components | 4 | 250 |
| M315 | Friction materials | 4 | 250 |
| M316 | Ring gear | 4 | 250 |
| M317 | Hose line clutch release systems | 4 | 250 |
| M320 | Elastomeric moulting material | 4 | 250 |
| M330 | Aluminium castings incl. machining | 4 | 250 |
| M340 | Bearing housings | 1 | 1000 |
| M341 | Investment casting | 4 | 250 |
| M342 | Iron castings | 0,13 | 7500 |
| M343 | Sintered parts | 4 | 250 |
| M345 | Extrusion parts | 4 | 250 |
| M346 | Brass cages | 4 | 250 |
| M350 | Stamped and drawn parts | 4 | 250 |
| M355 | Springs | 4 | 250 |
| M360 | Turned and milled parts | 4 | 250 |
| M370 | Electromechanics | 4 | 250 |
| M380 | Job shops | 4 | 250 |
| M381 | Surface treatment | 4 | 250 |
| M382 | Heat treatment | 4 | 250 |
| M392 | Traded goods | 4 | 250 |
| M393 | Rolling bearings (balls, needles, rolls) | 4 | 250 |
| M394 | Plain bearings | 4 | 250 |

# Text boxes

Ratio of complaints to goods receipt items

100

10

10

1

5

0

%

90

1

QZ 1

10

20

%

0

2

50

1

QZ 4

90

100

Ratio of complaints to goods receipt items

100

10

10

1

5

0

%

90

1

LZ 3

Ratio of logistics complaints to goods receipt items